## Slide 1
Introduction to Arduino Microcontrollers
Notes: *

## Slide 2: What is a Microcontroller ? What is a Microprocessor ?
A Microcontroller (8 bit) does one task very fast and very well, like a cell phone, microwave, house alarm, etc. It's does one program over and over again and never changes, programed stored in ROM and has all I/O support hardware onboard the chip. Can be very low power i.e. Thermostat - Nano Watts!
A microprocessor (32/64 Bit) on the other hand can run multiple programs and change programs, just like your PC. Does very large complex programs and very complex math and has external I/O support like video cards, audio, lan, etc. and storage on large disk. Is a power hog! 500Watts!
The line is blurring between these two. For example ARM processors (32 Bit) for example used in a smart phone. These microcontrollers are so powerful they run multiple programs very similar to microprocessor but keep the low power characteristic of a microcontroller

## Slide 3: What is Arduino?
Physical computing platform
Open source
“Hardware Abstracted” Wiring Language-similar to ‘C’
USB programmable
Large community
Multi platform Win/Mac/Linux
Inexpensive
€20 Radionics

## Slide 4: What is Arduino?
Based on ATmega328 – 8 BIT
w. USB interface
Voltage regulator (5V)
Specs
  RISC @ 16 MHz, 20 MIPS
  32 K Memory (.5K bootloader)
  6 Ch. 10 Bit A/D
  6 Ch. PWM, I2C, SPI
The “popularity” is in:
- Standard board design
- Wiring language
- Open Source

## Slide 5: Arduino Board Overview

## Slide 6
Digital IO (LEDs, switches)
Analog IO (resistive sensor data)
Serial Connection (Sensors, GPS, etc.)
Program from your computer
Your limit is only your creativity!
What do these do?
Notes: *
The digital inputs and outputs can sample a digital high or low signal and can sample voltage. These can be used with resistance-based sensors, such as thermistors, force sensors, light sensors, etc.
Analog inputs can input or output a stream of data. This is useful for things like GPS, data logging.

## Slide 7
Terminology
  I/O Board - main microcontroller
  Shield - add-on boards
  Sketch - the program
  Sensor - components (thermistors, etc.)
  Modules - serial data (GPS module, etc.)
Notes: *
The primary terms you need to know are what the I/O Board is, what a shield is, and what a sketch is.
The I/O Board is the "brains" of the operation. You program these from your computer.
A Shield is a device that plugs into an I/O Board. These extend the capabilities of the I/O Board.
A Sketch is a program written for the board and shields.

## Slide 8
14 current boards
Arduino I/O Boards
Notes: *
These are some of the various Arduino I/O boards. Clockwise from the top left is an Uno (great starter board), a Lilypad (normally used for clothing applications), a Pro (very small), a Mega (very powerful), and an Ethernet Board.
These boards all have analog and digital input/output. The Uno and Mega have the USB programming interface included - the other boards need an additional board to plug in (or solder in) to program.
There are more boards than just these!
The prices for these run as low as $20, as high as $60. The Uno is $30, which is generally the best place to start.

## Slide 9
Shields
Notes: *
Shields connect to the I/O board to extend it's functionality. Hundreds of shields are available, and you can make your own.
Starting from the upper left going clockwise:
Bluetooth Shield
Color LCD Shield
GPS Shield
Power Driver Shield (connects to a computer power supply).
Shields can run as low as $15, as high as $200.
Bluetooth $40-$65
LCD: $40
GPS: $80
Power Driver: $20

## Slide 10: Shields

## Slide 11
Touchscreen Shield
Wave Shield
Datalogging Shield
Shields
Notes: *
The shield on the left is a touchscreen shield, the upper right is a light and temperature shield, and the lower right is a sound (music) shield.

## Slide 12
Ethernet Shield
XBee Shield
WiFi Shield
More Shields…
Notes: *
Communication shields - XBee, Ethernet, and WiFi (2.5 Ghz).
These run around $60-$80.

## Slide 13
Gas Sensor
Temp & Humidity
Flex Sensor
Fingerprint Scanner
Geiger Counter
Sensors
Notes: *
Shields aren't the only way to extend an Arduino board - you can hook sensors to it! These are some of the hundreds (if not thousands) available. Many of these are not made specifically for Arduino - some sensors, such as thermistors, you can get from Radio Shack and wire them in!
Sensors can run as low as $0.95 (for a thermistor or light sensor) to $150 (Geiger counter sensor)

## Slide 14
Photo/thermistor, infrared, force sensitive resistor, Hall effect, Piezo, tilt sensor..
Sensors
Notes: *

## Slide 15
Sketches
void setup()
void loop()
Globals
Includes
Notes: *
Sketches are built in the Arduino Development Kit. The dev kit is free and open source. It is basically a simplified C++ processor.
The sketch is then uploaded to the Arduino I/O board and will run.

## Slide 16: Binary
A switch has 2 positions; ON or OFF
In binary, we call these ; 1 or 0
There are 2 states so
  Instead of counting in 10’s (decimal) we count in 2’s.

## Slide 17: Binary
Decimal: 5632 =
        5x1000 + 6x100 + 3x10 + 2x1
        5x103 + 6x102 + 3x101 + 2x100
Binary: 101110 =
1x25 + 0x24 + 1x23 + 1x22 + 1x21 + 0x20
32 + 0 + 8 + 4 + 2 + 0

## Slide 18: Breadboard

## Slide 21: Convert decimal (X) to binary. X/8 or X/23 Ans = 1 hence D = HIGH Ans = 0 hence D = LOW X%8 = decimal for 3 LSB's remaining Repeat above
X D C B A
0 0 0 0 0
1 0 0 0 1
2 0 0 1 0
3 0 0 1 1
4 0 1 0 0
5 0 1 0 1
6 0 1 1 0
7 0 1 1 1
8 1 0 0 0
9 1 0 0 1