## Slide 1
By Confey College
Confey CAN!

## Slide 2: Project Overview
The TEAM
CanSat Construction
Programming and Coding
Testing and Calibration
Parachute Construction
Community Outreach
Data Analysis

## Slide 3: The Team and the wider team:
Liam – Outreach/Communication (TL)
Conor – Calibration/Construction
Gergely – Software/Data presentation
Julia – Parachute Analysis/Design/Construction
Alex – Data analysis/Presentation
Naoise, Denis, Kieran, William…

## Slide 4: Primary and Secondary Mission
Satellite location via GPS and LED’s
Look at Pressure Vs Altitude
Temperature Vs Altitude
Humidity Vs Altitude
gForces experienced during flight
Vertical Velocity over time
Link video of flight with graphs

## Slide 5: Original Cansat Construction
- Plastic coated metal frame
  in a
polycarbonate casing
On/off switch

## Slide 6: Secondary Mission – Signal LOSS:
Plastic coated Metal
 changed to
Smaller PolyCarb spine

## Slide 7: Secondary Mission GPS Signal LOSS:
modified shield headers so GPS shield sits on top

## Slide 8: Fitting the sensors into PCB:
accelerometer
Relative Humidity
BMP180Pressure

## Slide 9: Testing and Calibration
Butler Transtest Calibrations(EU)CE:
-Thermistor
(industrial temperature regulator)
-Pressure Sensor (sealed lunch box and
pressure pump )

## Slide 10: Thermistor Calibration Data
Chart: Temperature Vs Voltage
| 4.83 | 4.81 | 4.79 | 4.78 | 4.76 | 4.75 | 4.74 | 4.73 | 4.72 | 4.71 | 4.689999999999999 | 4.649999999999998 | 4.64 | 4.63 | 4.619999999999996 | 4.609999999999998 | 4.58 | 4.58 | 4.56 | 4.55 | 4.54 | 4.53 | 4.52 | 4.51 | 4.5 | 4.49
"Temp Vs Voltage" | 7.3 | 9.2 | 12.1 | 13.3 | 15.1 | 15.8 | 16.7 | 17.4 | 18.2 | 19 | 20.1 | 23.1 | 23.1 | 24.7 | 24.8 | 25.4 | 26.5 | 26.5 | 27.8 | 28.3 | 28.8 | 29.2 | 29.9 | 30.4 | 30.9 | 31.4
Formula used in Arduino
program
* Different thermistor to kit

## Slide 11: Further Calibration:
BMP180 Barometric Pressure/Temp sensor
Pressure: against MPX4115A
Temperature
– Hairdryer/Freezer

## Slide 12: BMP180 Calibration:
Chart: BMP180Temp Calibration
| 25.4 | 25.82 | 25.96 | 26.05 | 26.14 | 26.22 | 26.33 | 26.45 | 26.62 | 26.9 | 27.25 | 27.64
"Sensor Temp" | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 35

## Slide 13: Further Calibration:
ADXL345 Accelerometer
* Tested All 3 axis in both directions - offset

## Slide 14: Further Calibration:
HIH4030 Relative Humidity sensor

## Slide 15: Power Consumption:
173.9 mA when running
9v Battery capacity 600mAh
650/173.9 = 3.73 hrs
BUT larger current lower capacity so unsure..
use 6 x 1.5V AA in series
Voltage regulator inefficient

## Slide 16: The Parachute – Terminal velocity
What affects Terminal velocity:
Area of material
Drag Coefficient
  Shape of parachute
  Cross, Hemispherical
  Polygon, Parapent
Weight (mg) of can
-Density of Air
11 m/s ≥Terminal velocity ≥ 8m/s
Cansat breaks
Cansat drifts

## Slide 17: The Parachute – Stabiliity (need can to stay upright)
What affects Stability :
  Strong fibres when ejecting (nylon)
- Strong fabric (ripstop)
- Hole(s) ??
- Mini central parachute

## Slide 18: Parachute testing
4 Prototypes
  - Cross, Hemispherical, 2 Octagons
Drone testing x 2
Lost one!
2 choices (weather)

## Slide 19: Outreach
Public Communications
- Butler tech –very willing to work with Confey students again!
- Contacted Dunnes Stores for sponsorship/prizes
Spoke with representatives from Intel/HP/Salesforce 2 Apple Macs were donated to CONFEYCAN
Have written article for two local newspapers
Local photographer used Quadcoptor

## Slide 20: Outreach
- Survey/Online Design Competition
-Team name
-Team logo
- 100’s of entries
Open day presentation
  800 attendees
5th Years attend launch
In our school ..

## Slide 21: Outreach
Website Construction
- Home Page
- Infomercial (ESERO)
- Survey competition
- Blog
- Photos/Videos

## Slide 22: Programming and Coding
Transmitting Data
-Rf Magic/Terminal
- Baud rates/loop delay
The wire Antenna
- our working frequency (444MHz)
- Length = c/4f = 3x108 = 0.169m
4 x 444 x 106

## Slide 23: Coding for secondary missions…
Not enough Analog i/ps
No room/time for a multiplexer
I2C protocol – share inputs
2 sensors could work with I2C
Added extra Pressure sensor (I2C)
3 A pins
1 A pin
1 A pin
2 A pins
1 A pin

## Slide 24: Coding continued….
SPI and I2C protocol
Found programs online (changed baudrate)
Copied and pasted..WORKED!
Edited to give the outputs we wanted

## Slide 25
Getting the Data cleaned up…….
canLOG.txt
Cleandata. txt
ConfeyCanData.xls
ARDUINO
program output
PYTHON
program

## Slide 26: Data Analysis:
Chart: Thermistor temp Vs BMP180

## Slide 27: Data Analysis:
Chart: Altitude (GPS Vs MP4115 Vs BMP180)

## Slide 28: Data Analysis:
Chart: Resultant g Force and Altitude(BMP)

## Slide 29
Data Analysis:
Chart: Pressure, Temp Vs Real Time for BMP180
Chart: Temperature and Pressure Vs Time

## Slide 30
Chart: Relative Humidity and Alitutude
Data Analysis:

## Slide 31
Improvements for EUROPE:
Increase parachute terminal velocity
Improve signal reception
More Flexible Wiring
Tidy code

## Slide 32
The BIG picture:
CanBot !

## Slide 33
Flexible Solar
Panels:
Additions for Europe:
To recharge
CanSat during/after landing
As a means of detecting Solar Radiation strength

## Slide 34
Additions for EUROPE:
2 Way
Communication:
CanSat to relay messages from planet/groundstation
Ground station to ‘talk’ to CanSat
(go to sleep)